## Slide 1: Machine-Level Programming I: Basics or Introduction to Computer Architecture CS154 Autumn 2019, Prof Chien Lecture 4 Sections 3.1-3.3

## Slide 2: Big Picture
Physics
Devices
Circuits
Gates
Register-Transfer Level
Microarchitecture
Instruction Set Architecture
Operating System/Virtual Machines
Programming Language
Algorithm
Application
Register-Transfer Level
Lecture Goals
Define ISA
Motivate the need for an ISA
Understand key instructions and components of an ISA
See examples of different ISAs

## Slide 3: Interfaces
A data type is:
state
+
methods
State is data
Methods are operations on data
These methods are the interface for the data object
Set_t
insert()
remove()
contains()

## Slide 4: Computer Architecture
Hardware
(Processor + Memory)
The architecture is the
interface
between software and hardware
State - contents of memory
(Note: different architectures may have different kinds of memory)
Methods - change memory
imull
xorl
movl
leal

## Slide 5: Example
void swap (int *xp, int *yp)
{
int t0 = *xp;
int t1 = *yp;
*xp = t1;
*yp = t0;
}
swap:
movl (%rdi), %rax
movl (%rsi), %rdx
movl %rdx, (%rdi)
movl %rax, (%rsi)
ret
Hardware
(Processor + Memory)

## Slide 6: Compatibility Problem at IBM
In early 1960’s, IBM had 4 incompatible lines of computers!
        701  7094
        650  7074
        702  7080
        1401  7010
Each system had its own
      Instruction set
      I/O system and Secondary Storage:
      magnetic tapes, drums and disks
      assemblers, compilers, libraries,...
      market niche business, scientific, real time, ...

## Slide 7: Compatibility Problem at IBM
By early 1960’s, IBM had 4 incompatible lines of computers!
        701  7094
        650  7074
        702  7080
        1401  7010
Each system had its own
      Instruction set
      I/O system and Secondary Storage:
      magnetic tapes, drums and disks
      assemblers, compilers, libraries,...
      market niche business, scientific, real time, ...

## Slide 8: Compatibility Problem at IBM
By early 1960’s, IBM had 4 incompatible lines of computers!
        701  7094
        650  7074
        702  7080
        1401  7010
Each system had its own
      Instruction set
      I/O system and Secondary Storage:
      magnetic tapes, drums and disks
      assemblers, compilers, libraries,...
      market niche business, scientific, real time, ...
 IBM 360

## Slide 9: IBM 360 : Design Premises Amdahl, Blaauw and Brooks, 1964
The design must lend itself to growth and successor machines
General method for connecting I/O devices
Total performance - answers per month rather than bits per microsecond  programming aids
Simple to assemble systems with redundant I/O devices, memories etc. for fault tolerance
…

## Slide 10: IBM 360: A General-Purpose Register (GPR) Machine
Processor State
  Memory + registers
  16 General-Purpose 32-bit Registers
  4 Floating Point 64-bit Registers
  A Program Status Word (PSW) -- a special register
    PC, Condition codes, Control flags
A 32-bit machine with 24-bit addresses
Data Formats
  8-bit bytes, 16-bit half-words, 32-bit words, 64-bit double-words

## Slide 11: IBM 360: A General-Purpose Register (GPR) Machine
Processor State
  Memory + registers
  16 General-Purpose 32-bit Registers
  4 Floating Point 64-bit Registers
  A Program Status Word (PSW) -- a special register
    PC, Condition codes, Control flags
A 32-bit machine with 24-bit addresses
Data Formats
  8-bit bytes, 16-bit half-words, 32-bit words, 64-bit double-words
The IBM 360 is why bytes are 8-bits long today!

## Slide 12: IBM 360: Initial Implementations
        Model 30 . . . Model 70
Storage 8K - 64 KB 256K - 512 KB
Datapath 8-bit 64-bit
Circuit Delay 30 nsec/level 5 nsec/level
Local Store Main Store Transistor Registers
Control Store Read only 1sec Conventional circuits
IBM 360 instruction set architecture (ISA) completely hid the underlying technological differences between various models.
Milestone: The first true ISA designed as portable hardware-software interface!

## Slide 13: IBM 360: Initial Implementations
        Model 30 . . . Model 70
Storage 8K - 64 KB 256K - 512 KB
Datapath 8-bit 64-bit
Circuit Delay 30 nsec/level 5 nsec/level
Local Store Main Store Transistor Registers
Control Store Read only 1sec Conventional circuits
IBM 360 instruction set architecture (ISA) completely hid the underlying technological differences between various models.
Milestone: The first true ISA designed as portable hardware-software interface!
With minor modifications it still survives today!

## Slide 14: From IBM 360 To The zSeries z11 Microprocessor
5.2 GHz in IBM 45nm PD-SOI CMOS technology
1.4 billion transistors in 512 mm2
64-bit virtual addressing
  original S/360 was 24-bit, and S/370 was 31-bit extension
Quad-core design
Three-issue out-of-order superscalar pipeline
Out-of-order memory accesses
Redundant datapaths
  every instruction performed in two parallel datapaths and results compared
64KB L1 I-cache, 128KB L1 D-cache on-chip
1.5MB private L2 unified cache per core, on-chip
On-Chip 24MB eDRAM L3 cache
Scales to 96-core multiprocessor with 768MB of shared L4 eDRAM
[ IBM, Kevin Shum, HotChips, 2010]
© International Business Machines Corporation.

## Slide 15: Engineering Aside
Architecture design is a tradeoff
On the one hand
  Want a compatible line of processors
  Don’t want to rewrite all software when new architecture available
On the other hand
  Need to maintain interface limits innovation

## Slide 16: Same Architecture Different Microarchitecture
AMD Phenom X4
X86 Instruction Set
Quad Core
125W
Decode 3 Instructions/Cycle/Core
64KB L1 I Cache, 64KB L1 D Cache
512KB L2 Cache
Out-of-order
2.6GHz
Intel Atom
X86 Instruction Set
Single Core
2W
Decode 2 Instructions/Cycle/Core
32KB L1 I Cache, 24KB L1 D Cache
512KB L2 Cache
In-order
1.6GHz
Image Credit: Intel
Image Credit: AMD

## Slide 17: Different Architecture Different Microarchitecture
AMD Phenom X4
X86 Instruction Set
Quad Core
125W
Decode 3 Instructions/Cycle/Core
64KB L1 I Cache, 64KB L1 D Cache
512KB L2 Cache
Out-of-order
2.6GHz
IBM POWER7
Power Instruction Set
Eight Core
200W
Decode 6 Instructions/Cycle/Core
32KB L1 I Cache, 32KB L1 D Cache
256KB L2 Cache
Out-of-order
4.25GHz
Image Credit: IBM
Image Credit: AMD
Courtesy of International Business Machines Corporation, © International Business Machines Corporation.

## Slide 18: Let’s Design an Architecture

## Slide 19: What Should Our Architecture Do?
ALU
What is the smallest number of instructions we have to support?
Does it support all high-level programming languages (e.g., C)?
Arithmetic and Logical Unit

## Slide 20: What Should Our Architecture Do?
ALU
sub a, b
Mem[b] = Mem[b] - Mem[a];
Execute next instruction;
Is this enough?

## Slide 21: The Bare Minimum
ALU
subleq a, b, c
Mem[b] = Mem[b] - Mem[a];
if (Mem[b] ≤ 0) goto c;
else execute next instruction;

## Slide 22: Example
If (a > b)
{
b = a
}
1. subleq x, x, .+1 # set x = 0
2. subleq a, x, .+1 # set x = -a
3. subleq y, y, .+1 # set y = 0
4. subleq x, y, .+1 # set y = a
5. subleq b, y, 10 # set y = a-b, jmp if a-b <= 0
6. subleq z, z, .+1 # set z = 0
7. subleq a, z, .+1 # set z = -a
8. subleq b, b, .+1 # set b = 0
9. subleq z, b, .+1 # set b = -z (a)
10.ret.
subleq a, b, c
Mem[b] = Mem[b] - Mem[a];
if (Mem[b] ≤ 0) goto c;
else execute next instruction;

## Slide 23: Where Do Operands Come from And Where Do Results Go?
ALU
Notes: By no means all configurations, Memory Memory.
For instance, Hybrid things, and Memory can be destination on some architectures.
This is just the logical abstraction, and by no means is how these things are implemented.

## Slide 24: Where Do Operands Come from And Where Do Results Go?
ALU
…
Memory
Notes: By no means all configurations, Memory Memory.
For instance, Hybrid things, and Memory can be destination on some architectures.
This is just the logical abstraction, and by no means is how these things are implemented.

## Slide 25: Where Do Operands Come from And Where Do Results Go?
Processor
…
ALU
…
Memory
Notes: By no means all configurations, Memory Memory.
For instance, Hybrid things, and Memory can be destination on some architectures.
This is just the logical abstraction, and by no means is how these things are implemented.

## Slide 26: Where Do Operands Come from And Where Do Results Go?
Notes: By no means all configurations, Memory Memory.
For instance, Hybrid things, and Memory can be destination on some architectures.
This is just the logical abstraction, and by no means is how these things are implemented.

## Slide 27: Where Do Operands Come from And Where Do Results Go?
…
TOS
ALU
Processor
…
Memory
Stack
Notes: By no means all configurations, Memory Memory.
For instance, Hybrid things, and Memory can be destination on some architectures.
This is just the logical abstraction, and by no means is how these things are implemented.

## Slide 28: Where Do Operands Come from And Where Do Results Go?
…
TOS
ALU
Processor
…
Memory
ALU
Processor
…
Memory
Stack
Accumulator
Notes: By no means all configurations, Memory Memory.
For instance, Hybrid things, and Memory can be destination on some architectures.
This is just the logical abstraction, and by no means is how these things are implemented.

## Slide 29: Where Do Operands Come from And Where Do Results Go?
…
TOS
ALU
Processor
…
Memory
ALU
Processor
…
Memory
ALU
Processor
…
Memory
…
Stack
Accumulator
Register-
Memory
Notes: By no means all configurations, Memory Memory.
For instance, Hybrid things, and Memory can be destination on some architectures.
This is just the logical abstraction, and by no means is how these things are implemented.

## Slide 30: Where Do Operands Come from And Where Do Results Go?
…
TOS
ALU
Processor
…
Memory
ALU
Processor
…
Memory
ALU
Processor
…
Memory
…
Stack
Accumulator
Register-
Memory
Register-
Register
ALU
Processor
…
Memory
…
Notes: By no means all configurations, Memory Memory.
For instance, Hybrid things, and Memory can be destination on some architectures.
This is just the logical abstraction, and by no means is how these things are implemented.

## Slide 31: Where Do Operands Come from And Where Do Results Go?
…
TOS
ALU
Processor
…
Memory
ALU
Processor
…
Memory
ALU
Processor
…
Memory
…
Stack
Accumulator
Register-
Memory
Register-
Register
ALU
Processor
…
Memory
0
1
…
2 or 3
Number Explicitly
Named Operands:
2 or 3
Notes: By no means all configurations, Memory Memory.
For instance, Hybrid things, and Memory can be destination on some architectures.
This is just the logical abstraction, and by no means is how these things are implemented.

## Slide 32: What are states and methods for these architectures?
…
TOS
ALU
Processor
…
Memory
ALU
Processor
…
Memory
ALU
Processor
…
Memory
…
Stack
Accumulator
Register-
Memory
Register-
Register
ALU
Processor
…
Memory
0
1
…
2 or 3
Number Explicitly
Named Operands:
2 or 3
Notes: By no means all configurations, Memory Memory.
For instance, Hybrid things, and Memory can be destination on some architectures.
This is just the logical abstraction, and by no means is how these things are implemented.

## Slide 33: Addressing Modes: How to Get Operands from Memory
Addressing Mode | Instruction | Function
Register | Add R4, R3, R2 | Regs[R4] <- Regs[R3] + Regs[R2] **
Immediate | Add R4, R3, #5 | Regs[R4] <- Regs[R3] + 5 **
Displacement | Add R4, R3, 100(R1) | Regs[R4] <- Regs[R3] + Mem[100 + Regs[R1]]
Register Indirect | Add R4, R3, (R1) | Regs[R4] <- Regs[R3] + Mem[Regs[R1]]
Absolute | Add R4, R3, (0x475) | Regs[R4] <- Regs[R3] + Mem[0x475]
Memory Indirect | Add R4, R3, @(R1) | Regs[R4] <- Regs[R3] + Mem[Mem[R1]]
PC relative | Add R4, R3, 100(PC) | Regs[R4] <- Regs[R3] + Mem[100 + PC]
Scaled | Add R4, R3, 100(R1)[R5] | Regs[R4] <- Regs[R3] + Mem[100 + Regs[R1] + Regs[R5] * 4]
** May not actually access memory!
Notes: Mention Immediate
Mention 3-register format

## Slide 34: ISA Encoding
Fixed Width: Every Instruction has same width
Easy to decode
(RISC Architectures: MIPS, PowerPC, SPARC, ARM…)
Ex: MIPS, every instruction 4-bytes
Variable Length: Instructions can vary in width
Takes less space in memory and caches
(CISC Architectures: IBM 360, x86, Motorola 68k, VAX…)
Ex: x86, instructions 1-byte up to 17-bytes

## Slide 35: Real World Instruction Sets
Arch | Type | # Oper | # Mem | Data Size | # Regs | Addr Size | Use
Alpha | Reg-Reg | 3 | 0 | 64-bit | 32 | 64-bit | Workstation
ARM | Reg-Reg | 3 | 0 | 32/64-bit | 16 | 32/64-bit | Cell Phones, Embedded
MIPS | Reg-Reg | 3 | 0 | 32/64-bit | 32 | 32/64-bit | Workstation, Embedded
SPARC | Reg-Reg | 3 | 0 | 32/64-bit | 24-32 | 32/64-bit | Workstation
TI C6000 | Reg-Reg | 3 | 0 | 32-bit | 32 | 32-bit | DSP
IBM 360 | Reg-Mem | 2 | 1 | 32-bit | 16 | 24/31/64 | Mainframe
x86 | Reg-Mem | 2 | 1 | 8/16/32/64-bit | 4/8/24 | 16/32/64 | Personal Computers
VAX | Mem-Mem | 3 | 3 | 32-bit | 16 | 32-bit | Minicomputer
Mot. 68k | Accum. | 1 | 1/2 | 8-bit | 0 | 16-bit | Microcontroller

## Slide 36: In summary…
Instruction Must Specify:
  What it does (the operation it performs)
  Where its operands come from (memory, registers, stack, etc)
  Type
    Integer or floating point
  Sometimes Width
    byte, word, double word, etc

## Slide 37: Big Picture
Physics
Devices
Circuits
Gates
Register-Transfer Level
Microarchitecture
Instruction Set Architecture
Operating System/Virtual Machines
Programming Language
Algorithm
Application
Register-Transfer Level
Instruction Set Architecture
Interfaces for controlling hardware
Commonly called Architecture
Software cannot directly see anything below this level
Notes: Bridging Abstractions!