## Slide 1: Caching Overview CS154, Autumn 2019, Prof Chien Intro to Computer Systems Lecture 11 Book Sections 6.4-6.5

## Slide 2: Lecture Goals
Last Lecture
  Review
  Fundamental tradeoff in memory: Big or Fast
  Locality of reference
Today
  Understand mechanics of caches
Physics
Devices
Circuits
Gates
Register-Transfer Level
Microarchitecture
Instruction Set Architecture
Operating System/Virtual Machines
Programming Language
Algorithm
Application
Register-Transfer Level

## Slide 3: Review: Memory Hierarchy
Regs
L1 cache
(SRAM)
Main memory
(DRAM)
Local secondary storage
(local disks)
Larger,
slower,
and
cheaper
(per byte)
storage
devices
Remote secondary storage
(e.g., Web servers)
Local disks hold files retrieved from disks
on remote servers
L2 cache
(SRAM)
L1 cache holds cache lines retrieved from the L2 cache.
CPU registers hold words retrieved from the L1 cache.
L2 cache holds cache lines
retrieved from L3 cache
L0:
L1:
L2:
L3:
L4:
L5:
Smaller,
faster,
and
costlier
(per byte)
storage
devices
L3 cache
(SRAM)
L3 cache holds cache lines
retrieved from main memory.
L6:
Main memory holds disk blocks retrieved from local disks.

## Slide 4: Review: Memory Hierarchy
Cache: Fundamental idea of a memory hierarchy:
  A smaller, faster memory that acts as a staging area for a subset of the data in a larger, slower memory
  For each k, the faster, smaller device at level k serves as a cache for the larger, slower device at level k+1.
Why do memory hierarchies work?
  Because of locality, programs tend to access the data at level k more often than they access the data at level k+1.
  Thus, the storage at level k+1 can be slower, and thus larger and cheaper per bit.
The memory hierarchy creates a large pool of storage that costs as much as the cheap storage near the bottom, but that serves data to programs at the rate of the fast storage near the top.

## Slide 5: SRAM vs. DRAM Tradeoff
SRAM (cache)
  Faster (L1 cache: a few CPU cycles)
  Smaller (Kilobytes (L1) or Megabytes (L2))
  More expensive and “energy-hungry”
DRAM (main memory)
  Relatively slower (hundreds of CPU cycles)
  Larger (Gigabytes)
  Cheaper

## Slide 6: Locality is everywhere
L1-L3 caches
Processor
(w/ Registers)
Big Slow
Memory
(DRAM)
Controlled by cache hardware
Controlled by compiler

## Slide 7: Locality: Common And Predictable Memory Reference Patterns
Temporal Locality:
If a location is
referenced it is likely
to be referenced again
in the near future
Spatial Locality:
If a location is
referenced it is likely
that locations near it
will be referenced in
the near future
sum = 0;
for (i = 0; i < n; i++)
sum += a[i];
return sum;
Example

## Slide 8: How caches exploit both types of locality?
Temporal Locality:
If a location is
referenced it is likely
to be referenced again
in the near future
Spatial Locality:
If a location is
referenced it is likely
that locations near it
will be referenced in
the near future
Exploit temporal locality by remembering the contents of recently accessed locations
Exploit spatial locality by fetching blocks of data around recently accessed locations

## Slide 9: General Cache Concepts
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Cache
Memory
Larger, slower, cheaper memory
viewed as partitioned into “blocks”
Data is copied in block-sized transfer units
called “cache blocks”
(Typical: 32, 64 bytes)
Smaller, faster, more expensive
memory caches a subset of
the blocks
4
4
4
10
10
10

## Slide 10: General Cache Concepts: Hit
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Data in block b is needed
Request: 14
14
Block b is in cache:
Hit!
The degree to which the cache exploits locality can be quantified as hit rate =
# hits / # accesses

## Slide 11: General Cache Concepts: Miss
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Data in block b is needed
Request: 12
Block b is not in cache:
Miss!
Block b is fetched from
memory
Request: 12
12
12
12
The degree to which the cache fails to exploit locality is its miss rate =
# misses / # accesses

## Slide 12: Basic Flow for a “Mem  Reg” mov
How to check if there’s a match?
Which block to replace?

## Slide 13: General Cache Design and Organization (S, E, B)
E lines per set
S = 2s sets
set
line (cache block)
0
1
2
B-1
tag
v
B = 2b bytes per cache block (the data)
Cache size:
C = S x E x B data bytes
valid bit

## Slide 14: Cache Read: How Do I Find My Data?
E lines per set
S = 2s sets
0
1
2
B-1
tag
v
valid bit
B = 2b bytes per cache block (the data)
t bits
s bits
b bits
Address of word:
tag
set
index
block
offset
data begins at this offset
Locate set
Check if any line in set has matching tag
Yes + line valid: hit
Locate data starting at offset
Notes: Locating set:
Can only be one set
Set number = Memory block number % number of sets

## Slide 15: Example: Direct mapped cache (E = 1)
S = 2s sets
Direct mapped: One block per set
Assume: cache block size 8 bytes (B=8, b=3)
t bits
01
100
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
find set
t bits
s bits
b bits
Address of word (8 bytes):
tag
set
index
block
offset
(s=2)
Notes: Ask: if s = 2, i.e., a total of 4 sets,
And the address is 8 bits, how many bits of tag there are?
Answer: 64 – 3 – 2 = 59

## Slide 16: Example: Direct mapped cache (E = 1)
t bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
match: assume yes = hit
valid? +
block offset
tag
Direct mapped: One block per set
Assume: cache block size 8 bytes
Set 1

## Slide 17: Example: Direct mapped cache (E = 1)
t bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
match: assume yes = hit
valid? +
int (4 Bytes) is here
block offset
No match: old block is evicted and replaced
Direct mapped: One block per set
Assume: cache block size 8 bytes

## Slide 18: Example: 2-way set associative cache
E = 2: Two blocks per set
Assume: cache block size 8 bytes
t bits
0…01
100
Address of short:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
find set

## Slide 19: Example: 2-way set associative cache
t bits
0…01
100
Address of short:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
compare both
valid? +
match: yes = hit
block offset
tag

## Slide 20: Example: 2-way set associative cache
t bits
0…01
100
Address of short int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
compare both
valid? +
match: yes = hit
block offset
short int (2 Bytes) is here
No match:
One block in set is selected for eviction and replacement

## Slide 21: Set Associativity Affects Data Placement
0
1
2
3
4
5
6
7
Direct
Mapped
2-way set
associative
fully
associative
0
1
2
3
Set #
Set #
More cache misses
Simpler lookups
Less cache misses
More complex lookups
line
set

## Slide 22: Other Basic Cache Design Considerations
Block Replacement:
  Which block should be replaced on a miss?
Write Strategy:
  What happens on a write?

## Slide 23: Block Replacement: Which block to vote off?
No choice in a direct mapped cache
In an associative cache, which block from set should be evicted when the set becomes full?
Random
Least Recently Used (LRU)
  LRU cache state must be updated on every access
  True implementation only feasible for small sets (2-way)
  Pseudo-LRU binary tree often used for 4-8 way
First In, First Out (FIFO) aka Round-Robin
  Used in highly associative caches
Not Most Recently Used (NMRU)
  FIFO with exception for most recently used block(s)

## Slide 24: Write Strategy: How are writes handled?
Cache Hit
  Write Through – write to memory immediately, generally higher traffic but simpler to design
  Write Back – write cache only, memory is written when evicted, dirty bit per block avoids unnecessary write backs, more complicated
Cache Miss
  No Write Allocate – only write to main memory
  Write Allocate – fetch block into cache, then write
Common Combinations
  Write Through & No Write Allocate (old)
  Write Back & Write Allocate (new)

## Slide 25: Cache Performance Metrics
Miss Rate
  Fraction of memory references not found in cache (misses / accesses) = 1 – hit rate
  Typical numbers (in percentages):
    3-10% for L1
    can be quite small (e.g., < 1%) for L2, depending on size, etc.
Hit Time
  Time to deliver a line in the cache to the processor
    includes time to determine whether the line is in the cache
  Typical numbers:
    4 clock cycle for L1
    10 clock cycles for L2
Miss Penalty
  Additional time required because of a miss
    typically 50-200 cycles for main memory (Trend: increasing!)

## Slide 26: Let’s think about those numbers
Huge difference between a hit and a miss
  Could be 100x, if just L1 and main memory
Would you believe 99% hits is twice as good as 97%?
  Consider: cache hit time of 1 cycle miss penalty of 100 cycles
  Average memory access time = hit time + miss rate * miss penalty
  97% hits: 1 cycle + 0.03 * 100 cycles = 4 cycles
  99% hits: 1 cycle + 0.01 * 100 cycles = 2 cycles
But.. Misses in caches are inevitable

## Slide 27: Categorizing Misses: The Three C’s
Compulsory (or cold) – first-reference to a block, occur even with infinite cache
Capacity – cache is too small to hold all data needed by program at a given time (refer to as the working set)
Conflict – misses that occur because of collisions, even when the cache is large enough
  E.g., referencing blocks 0, 8, 0, 8, 0, 8 … would always miss if 0 and 8 are mapped to the same cache line in a large direct-mapped cache

## Slide 28: Direct-mapped cache simulation
M= 4 bit addresses, B=2 bytes/block,
S=4 sets, E=1 Blocks/set
Address trace (reads, one byte per read):
0 [00002],
1 [00012],
7 [01112],
8 [10002],
0 [00002]
x
t=1
s=2
b=1
xx
x
0
?
?
v
Tag
Block
miss [cold]
1
0
M[0-1]
hit
miss [cold]
1
0
M[6-7]
miss [cold]
1
1
M[8-9]
miss [conflict]
1
0
M[0-1]
Set 0
Set 1
Set 2
Set 3
Spatial Locality
Temporal Locality
(Unexploited)

## Slide 29: 2-way set associative cache simulation
M=4-bit addresses, B=2 bytes/block,
S=2 sets, E=2 blocks/set
Address trace (reads, one byte per read):
0 [00002],
1 [00012],
7 [01112],
8 [10002],
0 [00002]
xx
t=2
s=1
b=1
x
x
0
?
?
v
Tag
Block
0
0
0
miss
1
00
M[0-1]
hit
miss
1
01
M[6-7]
miss
1
10
M[8-9]
hit
Set 0
Set 1
Spatial Locality
Temporal Locality
(Exploited)

## Slide 30: Software View of Architecture State
Data
Instructions
CPU
Programmer-Visible State
  Does NOT change when we add caches
Contrast with microarchitecture state
  Microarchitecture is the specific implementation of an ISA
    HW designer decides what the microarchitecture looks like
  Caches: part of the microarchitecture state
PC
Registers
Memory
Object Code
Program Data
OS Data
Addresses
Stack
Condition
Codes
ALU

## Slide 31: What Have We Covered So Far?
Physics
Devices
Circuits
Gates
Register-Transfer Level
Microarchitecture
Instruction Set Architecture (ISA)
Operating System/Virtual Machines
Programming Language
Algorithm
Application
Register-Transfer Level
%rip
L1 cache
memory address bits
Is the following part of Architecture or Microarchitecture?
cache valid bits
Notes: Interface between SW and HW

## Slide 32: Real Stuff: Intel Core i7 Cache Hierarchy
Regs
L1
d-cache
L1
i-cache
L2 unified cache
Core 0
Regs
L1
d-cache
L1
i-cache
L2 unified cache
Core 3
…
L3 unified cache
(shared by all cores)
Main memory
Processor package
L1 i-cache and d-cache:
  32 KB, 8-way (E=8),
  Access: 4 cycles
L2 unified cache:
  256 KB, 8-way,
  Access: 11 cycles
L3 unified cache:
  8 MB, 16-way,
  Access: 30-40 cycles
Block size: 64 bytes for all caches.
(E=8)*(B=64)*(S=64)=32K

## Slide 33: Summary
First example of microarchitecture
  Can change cache structure without changing interface
  Allows us to make a range of processors with different cost/performance tradeoffs
Cache Basics
  Where can a block go?
  How do I find it?
  How to replace blocks?
  What about writes?
Critical Issue
  Even when code has locality, cache structure might fail to exploit it