## Slide 1: Machine-Level Programming I: Basics of Instruction Set Architecture CS154 Spring 2020 Section 3.1-3.5 Junchen Jiang
Announcement: HW1 is due tonight (4/13 11:59pm Central Time)
Submit HW via svn to your repository:
<CNETID>-cs154-spr-20/hw1/hw1.pdf or
<CNETID>-cs154-spr-20/hw1/hw1.txt

## Slide 2: Big Picture
Physics
Devices
Circuits
Gates
Register-Transfer Level
Microarchitecture
Instruction Set Architecture (ISA)
Operating System/Virtual Machines
Programming Language
Algorithm
Application
Register-Transfer Level
Lecture Goals
Define Instruction Set Architecture (ISA) and motivate the need for ISA
Basics of x86-64 ISA
Notes: ISA has two levels of meanings.
from a software perspective, ISA is the lowest-level programming interface exposed to software programmers.
from a hardware perspective, ISA is a set of functions that should be realized by hardware (including CPU and memory).

## Slide 3: Interfaces
A data type is:
state
+
methods
State is data
Methods are operations on data
These methods are the interface for the data object
Set_t
insert()
remove()
contains()
Notes: first understand what an interface is.
Collectively, these methods are called the interface of this object.
The key idea here is that the interface is entirely independent to the internal implementation of the object.
an interface completely separates the internal implementation from the external behaviors.

## Slide 4: Instruction Set Architecture (Computer Architecture)
Hardware
(Processor + Memory)
The architecture is the
interface
between software and hardware
State - contents of memory
(Note: different architectures may have different kinds of memory)
Methods - change memory
imulq
xorq
movq
leaq
Notes: Now, computer architecture or instruction set architecture is essentially an interface.
It also exposes some interface that allows programs to changes these internal states.

## Slide 5: Example
void swap (long *xp, long *yp)
{
long t0 = *xp;
long t1 = *yp;
*xp = t1;
*yp = t0;
}
swap:
movq (%rdi), %rax
movq (%rsi), %rdx
movq %rdx, (%rdi)
movq %rax, (%rsi)
ret
Hardware
(Processor + Memory)
mulq
xorq
movq
leaq
Assembly code

## Slide 6: Why is ISA needed?
Early days of computer systems
Hardware
Processor & Memory
Software
Hardware
Processor & Memory
Software
Hardware
Processor & Memory
Software
…
In 1960’s, IBM had 4 incompatible lines of computers

## Slide 7: Why is ISA needed?
Early days of computer systems
Hardware
Processor & Memory
Software
Hardware
Processor & Memory
Software
Hardware
Processor & Memory
Software
…
Hardware
Processor & Memory
Software
Hardware
Processor & Memory
Software
Hardware
Processor & Memory
Software
Instruction Set Architecture (ISA)
…
…
Faster innovation with ISA
Success of IBM 360
(general-purpose registers)

## Slide 8: IBM 360: Initial Implementations
        Model 30 . . . Model 70
Storage 8K - 64 KB 256K - 512 KB
Datapath 8-bit 64-bit
Circuit Delay 30 nsec/level 5 nsec/level
Local Store Main Store Transistor Registers
Control Store Read only 1sec Conventional circuits
IBM 360 instruction set architecture (ISA) completely hid the underlying technological differences between various models.
Milestone: The first true ISA designed as portable hardware-software interface!

## Slide 9: Engineering Aside
Architecture (interface) design is a tradeoff
On the one hand
  Want a compatible line of processors
  Don’t want to rewrite all software when new architecture available
On the other hand
  Need to maintain interface limits innovation

## Slide 10: Big Picture
Physics
Devices
Circuits
Gates
Register-Transfer Level
Microarchitecture
Instruction Set Architecture (ISA)
Operating System/Virtual Machines
Programming Language
Algorithm
Application
Register-Transfer Level
Lecture Goals
Define Instruction Set Architecture (ISA) and motivate the need for ISA
Basics of x86-64 ISA
  Register and mov instruction
  More instructions

## Slide 11: Software View of Memory
Data
Instructions
CPU
Programmer-Visible State of CPU
  Registers
    Heavily used program data
  Condition codes
    Store status information about most recent arithmetic operation
    Used for conditional branching
  PC: Program counter
    Address of next instruction
    Called “EIP” (IA32) or “RIP” (x86-64)
PC
Registers
Memory
Object Code
Program Data
OS Data
Addresses
Stack
Condition
Codes
  Memory
    Byte addressable array
    Code, user data, (some) OS data
    Includes stack used to support procedures
ALU

## Slide 12: Software View of Memory
Data
Instructions
CPU
Programmer-Visible State of CPU
  Registers
    Heavily used program data
  Condition codes
    Store status information about most recent arithmetic operation
    Used for conditional branching
  PC: Program counter
    Address of next instruction
    Called “EIP” (IA32) or “RIP” (x86-64)
PC
Registers
Memory
Object Code
Program Data
OS Data
Addresses
Stack
Condition
Codes
  Memory
    Byte addressable array
    Code, user data, (some) OS data
    Includes stack used to support procedures
ALU

## Slide 13: Example
void swap
(long *xp, long *yp)
{
long t0 = *xp;
long t1 = *yp;
*xp = t1;
*yp = t0;
}
swap:
movq (%rdi), %rax
movq (%rsi), %rdx
movq %rdx, (%rdi)
movq %rax, (%rsi)
ret

## Slide 14: x86-64 Integer Registers
  64-bit long (word size)
    Can reference low-order 4 bytes (also low-order 1 & 2 bytes)
  General-purpose registers (except %rsp)
%rsp
%eax
%ebx
%ecx
%edx
%esi
%edi
%esp
%ebp
%r8d
%r9d
%r10d
%r11d
%r12d
%r13d
%r14d
%r15d
%r8
%r9
%r10
%r11
%r12
%r13
%r14
%r15
%rax
%rbx
%rcx
%rdx
%rsi
%rdi
%rbp
Notes: Registers are special places in the CPU that can be used to hold heavily used program data.
First, registers are 64-bit wide
You can also access the lower-order 4 bytes with special names.
Second, they are general-purpose (except %rsp).

## Slide 15: Moving Data
Moving Data
  movq Source, Dest
Operand Types
  Immediate: Constant integer data
    Example: $0x400, $-533
    Like C constant, but prefixed with ‘$’
    Encoded with 1, 2, or 4 bytes
  Register: One of 16 integer registers
    Example: %rax, %r13
    But %rsp reserved for special use
    Others have special uses for particular instructions
  Memory: 8 consecutive bytes of memory at address given by register
    Simplest example: (%rax)
    Various other “address modes”
%rax
%rcx
%rdx
%rbx
%rsi
%rdi
%rsp
%rbp
%r8
%r9
%r10
%r11
%r12
%r13
%r14
%r15
Notes: how to move data between registers and memory?
The source and destination can be one of the three kinds:

## Slide 16: movq Operand Combinations
Cannot do memory-memory transfer with a single instruction
movq
Imm
Reg
Mem
Reg
Mem
Reg
Mem
Reg
Source
Dest
C Analog
movq $0x4,%rax
temp = 0x4;
movq $-147,(%rax)
*p = -147;
movq %rax,%rdx
temp2 = temp1;
movq %rax,(%rdx)
*p = temp;
movq (%rax),%rdx
temp = *p;
Src,Dest
Notes: Now, if you put them together, there are five combinations.
Note that there are some combinations among these three types that are not supported in x86-64

## Slide 17: General rules
Most instructions in x86 have a Source and Dest
Source is listed before Dest
Source is not modified
Dest is modified
Dest may be both operand and result
At most one of Source, Dest can be memory
Notes: We will see many other x86 instructions later, but they share some basic rules with the move instruction.

## Slide 18: Example of Simple Addressing Modes
void swap
(long *xp, long *yp)
{
long t0 = *xp;
long t1 = *yp;
*xp = t1;
*yp = t0;
}
swap:
movq (%rdi), %rax
movq (%rsi), %rdx
movq %rdx, (%rdi)
movq %rax, (%rsi)
ret

## Slide 19: Understanding Swap()
%rdi
%rsi
%rax
%rdx
void swap
(long *xp, long *yp)
{
long t0 = *xp;
long t1 = *yp;
*xp = t1;
*yp = t0;
}
Memory
Register Value
%rdi xp
%rsi yp
%rax t0
%rdx t1
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret
Registers

## Slide 20: Understanding Swap()
123
456
%rdi
%rsi
%rax
%rdx
0x120
0x100
Registers
Memory
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret
0x120
0x118
0x110
0x108
0x100
Address
Register Value
%rdi xp
%rsi yp
%rax t0
%rdx t1

## Slide 21: Understanding Swap()
123
456
%rdi
%rsi
%rax
%rdx
0x120
0x100
123
Registers
Memory
0x120
0x118
0x110
0x108
0x100
Address
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret
Register Value
%rdi xp
%rsi yp
%rax t0
%rdx t1

## Slide 22: Understanding Swap()
123
456
%rdi
%rsi
%rax
%rdx
0x120
0x100
123
456
Registers
Memory
0x120
0x118
0x110
0x108
0x100
Address
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret
Register Value
%rdi xp
%rsi yp
%rax t0
%rdx t1

## Slide 23: Understanding Swap()
456
456
%rdi
%rsi
%rax
%rdx
0x120
0x100
123
456
Registers
Memory
0x120
0x118
0x110
0x108
0x100
Address
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret
Register Value
%rdi xp
%rsi yp
%rax t0
%rdx t1
Notes: Notice that after changing the memory at address 0x120, its original value is still saved in register rax.

## Slide 24: Understanding Swap()
456
123
%rdi
%rsi
%rax
%rdx
0x120
0x100
123
456
Registers
Memory
0x120
0x118
0x110
0x108
0x100
Address
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret
Register Value
%rdi xp
%rsi yp
%rax t0
%rdx t1

## Slide 25: Simple Memory Addressing Modes
Normal (R) Mem[Reg[R]]
  Register R specifies memory address
  Aha! Pointer dereferencing in C movq (%rcx),%rax
Displacement D(R) Mem[Reg[R]+D]
  Register R specifies start of memory region
  Constant displacement D specifies offset movq 8(%rbp),%rdx

## Slide 26: Complete Memory Addressing Modes
Most General Form
D(Rb,Ri,S) Mem[Reg[Rb]+S*Reg[Ri]+ D]
  D: Constant “displacement” 1, 2, or 4 bytes (default 0, if omitted)
  Rb: Base register: Any of 16 integer registers (default 0, if omitted)
  Ri: Index register: Any, except for %rsp (default 0, if omitted)
  S: Scale: 1, 2, 4, or 8 (to align with typical element size in an array)
  (default 1, if omitted)
Special Cases
D(Rb) Mem[Reg[Rb]+D] (Displacement)
(Rb,Ri) Mem[Reg[Rb]+Reg[Ri]]
D(Rb,Ri) Mem[Reg[Rb]+Reg[Ri]+D]
(Rb,Ri,S) Mem[Reg[Rb]+S*Reg[Ri]]

## Slide 27: Address Computation Examples
Expression | Address Computation | Address
0x8(%rdx) |  | 
(%rdx,%rcx) |  | 
(%rdx,%rcx,4) |  | 
0x80(,%rdx,2) |  | 
Expression | Address Computation | Address
0x8(%rdx) | 0xf000 + 0x8 | 0xf008
(%rdx,%rcx) | 0xf000 + 0x100 | 0xf100
(%rdx,%rcx,4) | 0xf000 + 4*0x100 | 0xf400
0x80(,%rdx,2) | 2*0xf000 + 0x80 | 0x1e080
%rdx | 0xf000
%rcx | 0x0100

## Slide 28: Big Picture
Physics
Devices
Circuits
Gates
Register-Transfer Level
Microarchitecture
Instruction Set Architecture (ISA)
Operating System/Virtual Machines
Programming Language
Algorithm
Application
Register-Transfer Level
Lecture Goals
Define Instruction Set Architecture (ISA) and motivate the need for ISA
Basics of x86-64 ISA
  Register and mov instruction
  More instructions

## Slide 29: Address Computation Instruction
leaq Src, Dst (load effective address)
  Src is address mode expression
  Set Dst to address denoted by expression
  E.g., leaq 4(%rdx,%rcx,2), %rax
Uses
  Computing addresses without a memory reference
    E.g., translation of p = &x[i];
  Computing arithmetic expressions of the form x + k*y
    k = 1, 2, 4, or 8
Example
long m3(long x)
{
return x*3;
}
leaq (%rdi,%rdi,2), %rax # t <- x+x*2
Converted to ASM by compiler:

## Slide 30: Difference between leaq and movq
0x3F1
%rdi
%rax
0x30
0x90
Registers
Memory
0x090
Address
movq (%rdi,%rdi,2), %rax
leaq (%rdi,%rdi,2), %rax
%rdi
%rax
0x30
0x3F1
Registers

## Slide 31: Some Arithmetic Operations
Two Operand Instructions:
  Format Computation
    addq Src,Dest Dest = Dest + Src
    subq Src,Dest Dest = Dest  Src
    imulq Src,Dest Dest = Dest * Src
    salq Src,Dest Dest = Dest << Src (Also called shlq)
    sarq Src,Dest Dest = Dest >> Src (Arithmetic)
    shrq Src,Dest Dest = Dest >> Src (Logical)
    xorq Src,Dest Dest = Dest ^ Src
    andq Src,Dest Dest = Dest & Src
    orq Src,Dest Dest = Dest | Src
Watch out for argument order!
No distinction between signed and unsigned int

## Slide 32: Some Arithmetic Operations
One Operand Instructions
    incq Dest Dest = Dest + 1
    decq Dest Dest = Dest  1
    negq Dest Dest =  Dest
    notq Dest Dest = ~Dest
See book for more instructions

## Slide 33: Computation without a memory reference
Converted to ASM by compiler:
long m12(long x)
{
return x*12;
}
leaq (%rdi,%rdi,2), %rax # t <- x+x*2
salq $2, %rax # return t<<2
long m3(long x)
{
return x*3;
}
leaq (%rdi,%rdi,2), %rax # t <- x+x*2

## Slide 34: Arithmetic Expression Example
Interesting Instructions
  leaq: address computation
  salq: shift
  imulq: multiplication
    But, only used once
long arith
(long x, long y, long z)
{
long t1 = x+y;
long t2 = z+t1;
long t3 = x+4;
long t4 = y * 48;
long t5 = t3 + t4;
long rval = t2 * t5;
return rval;
}
arith:
leaq (%rdi,%rsi), %rax
addq %rdx, %rax
leaq (%rsi,%rsi,2), %rdx
salq $4, %rdx
leaq 4(%rdi,%rdx), %rcx
imulq %rcx, %rax
ret

## Slide 35: Understanding Arithmetic Expression Example
long arith
(long x, long y, long z)
{
long t1 = x+y;
long t2 = z+t1;
long t3 = x+4;
long t4 = y * 48;
long t5 = t3 + t4;
long rval = t2 * t5;
return rval;
}
arith:
leaq (%rdi,%rsi), %rax # t1
addq %rdx, %rax # t2
leaq (%rsi,%rsi,2), %rdx
salq $4, %rdx # t4
leaq 4(%rdi,%rdx), %rcx # t5
imulq %rcx, %rax # rval
ret
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rdx | Argument z,t4
%rax | t1, t2, rval
%rcx | t5

## Slide 36: Understanding Arithmetic Expression Example
long arith
(long x, long y, long z)
{
long t1 = x+y;
long t2 = z+t1;
long t3 = x+4;
long t4 = y * 48;
long t5 = t3 + t4;
long rval = t2 * t5;
return rval;
}
arith:
leaq (%rdi,%rsi), %rax # t1
addq %rdx, %rax # t2
leaq (%rsi,%rsi,2), %rdx
salq $4, %rdx # t4
leaq 4(%rdi,%rdx), %rcx # t5
imulq %rcx, %rax # rval
ret
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rdx | Argument z
%rax | t1
%rcx | 

## Slide 37: Understanding Arithmetic Expression Example
long arith
(long x, long y, long z)
{
long t1 = x+y;
long t2 = z+t1;
long t3 = x+4;
long t4 = y * 48;
long t5 = t3 + t4;
long rval = t2 * t5;
return rval;
}
arith:
leaq (%rdi,%rsi), %rax # t1
addq %rdx, %rax # t2
leaq (%rsi,%rsi,2), %rdx
salq $4, %rdx # t4
leaq 4(%rdi,%rdx), %rcx # t5
imulq %rcx, %rax # rval
ret
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rdx | Argument z
%rax | t1, t2
%rcx | 

## Slide 38: Understanding Arithmetic Expression Example
long arith
(long x, long y, long z)
{
long t1 = x+y;
long t2 = z+t1;
long t3 = x+4;
long t4 = y * 48;
long t5 = t3 + t4;
long rval = t2 * t5;
return rval;
}
arith:
leaq (%rdi,%rsi), %rax # t1
addq %rdx, %rax # t2
leaq (%rsi,%rsi,2), %rdx
salq $4, %rdx # t4
leaq 4(%rdi,%rdx), %rcx # t5
imulq %rcx, %rax # rval
ret
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rdx | Argument z,t4
%rax | t1, t2
%rcx | 
Notes: Notice that the lines in C code doesn’t have a 1-to-1 mapping to the lines in assembly.

## Slide 39: Understanding Arithmetic Expression Example
long arith
(long x, long y, long z)
{
long t1 = x+y;
long t2 = z+t1;
long t3 = x+4;
long t4 = y * 48;
long t5 = t3 + t4;
long rval = t2 * t5;
return rval;
}
arith:
leaq (%rdi,%rsi), %rax # t1
addq %rdx, %rax # t2
leaq (%rsi,%rsi,2), %rdx
salq $4, %rdx # t4
leaq 4(%rdi,%rdx), %rcx # t5
imulq %rcx, %rax # rval
ret
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rdx | Argument z,t4
%rax | t1, t2
%rcx | t5

## Slide 40: Understanding Arithmetic Expression Example
long arith
(long x, long y, long z)
{
long t1 = x+y;
long t2 = z+t1;
long t3 = x+4;
long t4 = y * 48;
long t5 = t3 + t4;
long rval = t2 * t5;
return rval;
}
arith:
leaq (%rdi,%rsi), %rax # t1
addq %rdx, %rax # t2
leaq (%rsi,%rsi,2), %rdx
salq $4, %rdx # t4
leaq 4(%rdi,%rdx), %rcx # t5
imulq %rcx, %rax # rval
ret
Register | Use(s)
%rdi | Argument x
%rsi | Argument y
%rdx | Argument z,t4
%rax | t1, t2, rval
%rcx | t5
Notes: it only uses add instruction and multiply instruction once each.
Instead, it heavily relies on the load effective address instruction.

## Slide 41: Different source/destination lengths
The suffix indicates the # of bytes to change/access
  q indicates 8 bytes, and l indicates 4 bytes
  For example, movq moves 8 bytes, and movl moves 4 bytes
  movq %rax, %rdx
  movl %eax, %edx
%rsp
%eax
%ebx
%ecx
%edx
%esi
%edi
%esp
%ebp
%r8d
%r9d
%r10d
%r11d
%r12d
%r13d
%r14d
%r15d
%r8
%r9
%r10
%r11
%r12
%r13
%r14
%r15
%rax
%rbx
%rcx
%rdx
%rsi
%rdi
%rbp

## Slide 42: Compiling Into Assembly
C Code (sum.c)
long plus(long x, long y);
void sumstore(long x, long y,
long *dest)
{
long t = plus(x, y);
*dest = t;
}
Generated x86-64 Assembly
sumstore:
pushq %rbx
movq %rdx, %rbx
call plus
movq %rax, (%rbx)
popq %rbx
ret
Example command
  gcc –Og –S sum.c
Produces file sum.s
Warning: Will get very different results on different machines due to different versions of gcc and different compiler settings.