## Slide 1: The Memory Hierarchy and Caches CS154, Spring 2020, Prof. Yanjing Li Intro to Computer Systems Book Sections 6.1-6.5

## Slide 2: Lecture Goals
Current topics:
  Intro to memory hierarchy
  Caches
Physics
Devices
Circuits
Gates
Register-Transfer Level
Microarchitecture
Instruction Set Architecture
Operating System/Virtual Machines
Programming Language
Algorithm
Application
Register-Transfer Level

## Slide 3: Some numbers
Instruction Type | Frequency
Memory  Register Move | 22%
Conditional Branch | 20%
Compare | 16%
Register  Memory Move | 12%
Add | 8%
And | 6%
Sub | 5%
Register  Register Move | 4%
Function call | 1%
Function return | 1%
Total | 96%
From H&P: Computer Architecture a Quantitative Approach
> 34% of instructions access data memory!
100% of instructions are stored in instruction memory!

## Slide 4: The CPU-Memory Gap
The gap widens between DRAM, disk, and CPU speeds.
Chart: Year
| 1985 | 1990 | 1995 | 2000 | 2003 | 2005 | 2010 | 2015
Disk seek time | 75000000 | 28000000 | 10000000 | 8000000 | 6000000 | 5000000 | 3000000 | 3000000
SSD access time | 50000
DRAM access time | 200 | 100 | 70 | 60 | 55 | 50 | 40 | 20
SRAM access time | 150 | 35 | 15 | 3 | 2.5 | 2 | 1.5 | 1.3
CPU cycle time | 166 | 50 | 6 | 1.6 | 0.3 | 0.5 | 0.4 | 0.33
Effective CPU cycle time | 0.3 | 0.25 | 0.1 | 0.08
DRAM
CPU
SSD
Disk

## Slide 5: Synthesize This
> 34% of instructions access data memory
100% of instructions access instruction memory
Memory is many orders of magnitude slower than the processor
  For example: Four-issue 2 GHz superscalar accessing 100 ns DRAM could execute 800 instructions during the time for one memory access!
These numbers don’t make sense

## Slide 6: There must be a way to speed up memory access!

## Slide 7: Why Are Memories Slow in the First Place?
Not all memories are slow
But, bigger means slower  Fundamental Tradeoff
  Technology differences
    Hard disk (slow) vs. SSD vs. DRAM vs. SRAM (fast)
  Just physics
    Signals in longer wires take longer to travel
Notes:     Slower technologies are cheaper, so they can be made bigger while are still affordable

## Slide 8: Key Idea: Memory Hierarchy
Regs
L1 cache
(SRAM)
Main memory
(DRAM)
Local secondary storage
(local disks)
Larger,
slower,
and
cheaper
(per byte)
storage
devices
Remote secondary storage
(e.g., Web servers)
Local disks hold files retrieved from disks
on remote servers
L2 cache
(SRAM)
L1 cache holds cache lines retrieved from the L2 cache.
CPU registers hold words retrieved from the L1 cache.
L2 cache holds cache lines
retrieved from L3 cache
L0:
L1:
L2:
L3:
L4:
L5:
Smaller,
faster,
and
costlier
(per byte)
storage
devices
L3 cache
(SRAM)
L3 cache holds cache lines
retrieved from main memory.
L6:
Main memory holds disk blocks retrieved from local disks.

## Slide 9: Memory Hierarchy
Capacity: Register << Cache << DRAM
Speed: Register >> Cache >> DRAM
On a data access:
  if data is in fast memory -> low-latency access (to cache or register)
  if data is not in fast memory -> long-latency access to DRAM
Small Fast
Memory
(Cache)
Processor
Big Slow
Memory
(DRAM)
Notes: Most of what a program needs would be from the DRAM (let’s focus on this part)

## Slide 10
CPU Core (incl L1, L2), L3, and DRAM
Intel Skylake Server
DRAM BANKS

## Slide 11: Why Does Memory Hierarchy Work?
Memory hierarchies only work if …
The small, fast memory actually stores data that is used/re-used by the processor at a given time
  Do they???

## Slide 12: Locality!
The key to bridging this CPU-Memory gap is a fundamental property of computer programs known as locality

## Slide 13: Locality
Principle of Locality: Programs tend to use data and instructions with addresses near or equal to those they have used recently
Temporal locality:
  Recently referenced items are likely to be referenced again in the near future
Spatial locality:
  Items with nearby addresses tend to be referenced close together in time

## Slide 14: Locality Example
Data references
  Reference array elements in succession (stride-1 reference pattern).
  Reference variable sum each iteration.
Instruction references
  Reference instructions in sequence.
  Cycle through loop repeatedly.
sum = 0;
for (i = 0; i < n; i++)
sum += a[i];
return sum;
Spatial locality
Temporal locality
Spatial locality
Temporal locality

## Slide 15: Locality Example
Claim: Being able to look at code and get a qualitative sense of its locality is a key skill for a professional programmer.
Question: Can you permute the loops so that the function scans the 3-d array a with a stride-1 reference pattern (and thus has good spatial locality)?
int sum_array_3d(int a[M][N][N])
{
int i, j, k, sum = 0;
for (i = 0; i < M; i++)
for (j = 0; j < N; j++)
for (k = 0; k < N; k++)
sum += a[k][i][j];
return sum;
}

## Slide 16: Now, Back to Memory Hierarchy
Why do memory hierarchies work?
  Because of locality, programs tend to access the data at level k more often than they access the data at level k+1.
  Thus, the storage at level k+1 can be slower, and thus larger and cheaper per bit.
The memory hierarchy creates a large pool of storage that costs as much as the cheap storage near the bottom, but that serves data to programs at the rate of the fast storage near the top.
Cache: Fundamental idea of a memory hierarchy:
  A smaller, faster memory that acts as a staging area for a subset of the data in a larger, slower memory
  For each k, the faster, smaller device at level k serves as a cache for the larger, slower device at level k+1.

## Slide 17: General Cache Concepts
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Cache
Memory
Larger, slower, cheaper memory
viewed as partitioned into “blocks”
Data is copied in block-sized transfer units
called “cache blocks”
(Typical: 32, 64 bytes)
Smaller, faster, more expensive
memory caches a subset of
the blocks
4
4
4
10
10
10

## Slide 18: General Cache Concepts: Hit
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Data in block b is needed
Request: 14
14
Block b is in cache:
Hit!
The degree to which the cache exploits locality can be quantified as hit rate =
# hits / # accesses

## Slide 19: General Cache Concepts: Miss
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Data in block b is needed
Request: 12
Block b is not in cache:
Miss!
Block b is fetched from
memory
Request: 12
12
12
12
The degree to which the cache fails to exploit locality is its miss rate =
# misses / # accesses

## Slide 20: Basic Flow for a “Mem  Reg” mov
How to check if there’s a match?
Which block to replace?

## Slide 21: General Cache Design and Organization (S, E, B)
E lines per set
S = 2s sets
set
line (cache block)
0
1
2
B-1
tag
v
B = 2b bytes per cache block (the data)
Cache size:
C = S x E x B data bytes
valid bit

## Slide 22: Cache Read: How Do I Find My Data?
E lines per set
S = 2s sets
0
1
2
B-1
tag
v
valid bit
B = 2b bytes per cache block (the data)
t bits
s bits
b bits
Address of word:
tag
set
index
block
offset
data begins at this offset
Locate set
Check if any line in set has matching tag
Yes + line valid: hit
Locate data starting at offset
Notes: Locating set:
Can only be one set
Set number = Memory block number % number of sets

## Slide 23: Example: Direct mapped cache (E = 1)
S = 2s sets
Direct mapped: One block per set
Assume: cache block size 8 bytes (B=8, b=3)
t bits
01
100
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
find set
t bits
s bits
b bits
Address of word (8 bytes):
tag
set
index
block
offset
(s=2)
Notes: Ask: if s = 2, i.e., a total of 4 sets,
And the address is 8 bits, how many bits of tag there are?
Answer: 64 – 3 – 2 = 59

## Slide 24: Example: Direct mapped cache (E = 1)
t bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
match: assume yes = hit
valid? +
block offset
tag
Direct mapped: One block per set
Assume: cache block size 8 bytes
Set 1

## Slide 25: Example: Direct mapped cache (E = 1)
t bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
match: assume yes = hit
valid? +
int (4 Bytes) is here
block offset
No match: old block is evicted and replaced
Direct mapped: One block per set
Assume: cache block size 8 bytes

## Slide 26: Example: 2-way set associative cache
E = 2: Two blocks per set
Assume: cache block size 8 bytes
t bits
0…01
100
Address of short:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
find set

## Slide 27: Example: 2-way set associative cache
t bits
0…01
100
Address of short:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
compare both
valid? +
match: yes = hit
block offset
tag

## Slide 28: Example: 2-way set associative cache
t bits
0…01
100
Address of short int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
compare both
valid? +
match: yes = hit
block offset
short int (2 Bytes) is here
No match:
One block in set is selected for eviction and replacement

## Slide 29: Set Associativity Affects Data Placement
0 1 2 3 4 5 6 7
0 1 2 3
Set Number
Cache
Direct
Mapped
0 1 2 3 4 5 6 7 8 9
1 1 1 1 1 1 1 1 1 1 0 1 2 3 4 5 6 7 8 9
2 2 2 2 2 2 2 2 2 2 0 1 2 3 4 5 6 7 8 9
3 3
0 1
Memory
Block number
Where can block 12 be placed?
2-way set
associative
fully
associative
Only into
set 4
(12 mod 8)
Anywhere
in set 0
(12 mod 4)
Anywhere
Notes: Each memory block is B bytes, B=2^b

## Slide 30: Other Basic Cache Design Considerations
Block Replacement:
  Which block should be replaced on a miss?
Write Strategy:
  What happens on a write?

## Slide 31: Block Replacement: Which block to vote off?
No choice in a direct mapped cache
In an associative cache, which block from set should be evicted when the set becomes full?
Random
Least Recently Used (LRU)
  LRU cache state must be updated on every access
  True implementation only feasible for small sets (2-way)
  Pseudo-LRU binary tree often used for 4-8 way
First In, First Out (FIFO) aka Round-Robin
  Used in highly associative caches
Not Most Recently Used (NMRU)
  FIFO with exception for most recently used block(s)

## Slide 32: Write Strategy: How are writes handled?
Cache Hit
  Write Through – write to memory immediately, generally higher traffic but simpler to design
  Write Back – write cache only, memory is written when evicted, dirty bit per block avoids unnecessary write backs, more complicated
Cache Miss
  No Write Allocate – only write to main memory
  Write Allocate – fetch block into cache, then write
Common Combinations
  Write Through & No Write Allocate (old)
  Write Back & Write Allocate (new)