## Slide 1: Cache Performance Analysis CS154, Spring 2020, Prof. Yanjing Li Intro to Computer Systems Book Sections 6.6-6.7

## Slide 2: Cache Performance Metrics
Miss Rate
  Fraction of memory references not found in cache (misses / accesses) = 1 – hit rate
  Typical numbers (in percentages):
    3-10% for L1
    can be quite small (e.g., < 1%) for L2, depending on size, etc.
Hit Time
  Time to deliver a line in the cache to the processor
    includes time to determine whether the line is in the cache
  Typical numbers:
    4 clock cycle for L1
    10 clock cycles for L2
Miss Penalty
  Additional time required because of a miss
    typically 50-200 cycles for main memory (Trend: increasing!)

## Slide 3: Let’s think about those numbers
Huge difference between a hit and a miss
  Could be 100x, if just L1 and main memory
Would you believe 99% hits is twice as good as 97%?
  Consider: cache hit time of 1 cycle miss penalty of 100 cycles
  Average memory access time = hit time + miss rate * miss penalty
  97% hits: 1 cycle + 0.03 * 100 cycles = 4 cycles
  99% hits: 1 cycle + 0.01 * 100 cycles = 2 cycles
But.. Misses in caches are inevitable

## Slide 4: Categorizing Misses: The Three C’s
Compulsory (or cold) – first-reference to a block, occur even with infinite cache
Capacity – cache is too small to hold all data needed by program at a given time (refer to as the working set)
Conflict – misses that occur because of collisions, even when the cache is large enough
  E.g., referencing blocks 0, 8, 0, 8, 0, 8 … would always miss if 0 and 8 are mapped to the same cache line in a large direct-mapped cache

## Slide 5: Direct-mapped cache simulation
M= 4 bit addresses, B=2 bytes/block,
S=4 sets, E=1 Blocks/set
Address trace (reads, one byte per read):
0 [00002],
1 [00012],
7 [01112],
8 [10002],
0 [00002]
x
t=1
s=2
b=1
xx
x
0
?
?
v
Tag
Block
miss [cold]
1
0
M[0-1]
hit
miss [cold]
1
0
M[6-7]
miss [cold]
1
1
M[8-9]
miss [conflict]
1
0
M[0-1]
Set 0
Set 1
Set 2
Set 3
Spatial Locality
Temporal Locality
(Unexploited)

## Slide 6: 2-way set associative cache simulation
M=4-bit addresses, B=2 bytes/block,
S=2 sets, E=2 blocks/set
Address trace (reads, one byte per read):
0 [00002],
1 [00012],
7 [01112],
8 [10002],
0 [00002]
xx
t=2
s=1
b=1
x
x
0
?
?
v
Tag
Block
0
0
0
miss
1
00
M[0-1]
hit
miss
1
01
M[6-7]
miss
1
10
M[8-9]
hit
Set 0
Set 1
Spatial Locality
Temporal Locality
(Exploited)

## Slide 7: Associativity vs. Cache Misses
0
1
2
3
4
5
6
7
Direct
Mapped
2-way set
associative
fully
associative
0
1
2
3
Set #
Set #
More cache misses
Simpler lookups
Less cache misses
More complex lookups
line
set

## Slide 8: Let’s analyze cache performance
Step #1: Address trace
Step #2: Simulate cache misses/hits
Initial values:
filter = 0x00
in = 0x10
int filter[4];
int apply_filter(int* in){}
8-bit address
32-byte data cache
Direct-mapped (E=1)
4 sets
What’s the hit rate?
int filter[4];
int apply_filter(int* in) {
int i;
int a = 0;
for (i = 0; i < 4; i++){
a += in[i]*filter[i];
}
return a;
}

## Slide 9: C code and Asm
int filter[4];
int apply_filter(int* in) {
int i;
int a = 0;
for (i = 0; i < 4; i++){
a += in[i]*filter[i];
}
return a;
}
apply_filter:
movq $0, %rax
movq $0, %rdx
.L2:
movl (%rdi,%rdx,4), %ecx
imull filter(,%rdx,4), %ecx
addl %ecx, %eax
addq $1, %rdx
cmpq $4, %rdx
jne .L2
ret

## Slide 10: Step 1: Write down the Address Trace
0x00
0x04
0x08
0x0C
Address
%rdi
0x10
filter
%rdx i | filter(,%rdx,4) &filter[i] | (%rdi,%rdx,4) &in[i]
0 | 0x00 | 0x10
1 | 0x04 | 0x14
2 | 0x08 | 0x18
3 | 0x0C | 0x1C
0x10
0x14
0x18
0x1C
for (i = 0; i < 4; i++){
a += in[i]*filter[i];
}
in

## Slide 11: How Does Our Address Trace Interact With the Cache?
8-bit addresses
32 Bytes Data Cache
Direct-Mapped (E=1)
4 Sets
How many bits for Block Offset?
How many bits for Set Index?
How many bits for Tag?

## Slide 12: How Does Our Address Trace Interact With the Cache?
8-bit addresses
32 Bytes Data Cache
Direct-Mapped (E=1)
4 Sets
How many bits for Block Offset? 3
How many bits for Set Index? 2
How many bits for Tag? 3
xxx
t=3
s=2
b=3
xx
xxx
Notes: C = B*E*S
Assume only 8-bits of address are used

## Slide 13: Step 2: Direct-mapped cache simulation
M= 8 bit addresses, B=8 bytes/block,
S=4 sets, E=1 Blocks/set
xxx
t=3
s=2
b=3
xx
xxx
What is the expected miss rate?
??%
Capacity Misses? Conflict Misses? Compulsory Misses?
%rdx i | filter(,%rdx,4) &filter[i] | (%rdi,%rdx,4) &in[i]
0 | 0x00: 000 00 000 | 0x10: 000 10 000
1 | 0x04: 000 00 100 | 0x14: 000 10 100
2 | 0x08: 000 01 000 | 0x18: 000 11 000
3 | 0x0C: 000 01 100 | 0x1C: 000 11 100
Notes: 50% all cold misses

## Slide 14: Direct-mapped cache simulation
0
?
?
v
Tag
Block
0
?
?
0
?
?
0
?
?
Set 0
Set 1
Set 2
Set 3
%rdx i | filter(,%rdx,4) &filter[i] | (%rdi,%rdx,4) &in[i]
0 | 0x00: 000 00 000 | 0x10: 000 10 000
1 | 0x04: 000 00 100 | 0x14: 000 10 100
2 | 0x08: 000 01 000 | 0x18: 000 11 000
3 | 0x0C: 000 01 100 | 0x1C: 000 11 100
M= 8 bit addresses, B=8 bytes/block,
S=4 sets, E=1 Blocks/set
xxx
t=3
s=2
b=3
xx
xxx

## Slide 15: Direct-mapped cache simulation
0
?
?
v
Tag
Block
0
?
?
0
?
?
0
?
?
Set 0
Set 1
Set 2
Set 3
miss
%rdx i | filter(,%rdx,4) &filter[i] | (%rdi,%rdx,4) &in[i]
0 | 0x00: 000 00 000 | 0x10: 000 10 000
1 | 0x04: 000 00 100 | 0x14: 000 10 100
2 | 0x08: 000 01 000 | 0x18: 000 11 000
3 | 0x0C: 000 01 100 | 0x1C: 000 11 100
M= 8 bit addresses, B=8 bytes/block,
S=4 sets, E=1 Blocks/set
xxx
t=3
s=2
b=3
xx
xxx

## Slide 16: Direct-mapped cache simulation
0
?
?
v
Tag
Block
0
?
?
1
000
0x10, 0x14
0
?
?
Set 0
Set 1
Set 2
Set 3
miss
%rdx i | filter(,%rdx,4) &filter[i] | (%rdi,%rdx,4) &in[i]
0 | 0x00: 000 00 000 | 0x10: 000 10 000
1 | 0x04: 000 00 100 | 0x14: 000 10 100
2 | 0x08: 000 01 000 | 0x18: 000 11 000
3 | 0x0C: 000 01 100 | 0x1C: 000 11 100
M= 8 bit addresses, B=8 bytes/block,
S=4 sets, E=1 Blocks/set
xxx
t=3
s=2
b=3
xx
xxx

## Slide 17: Direct-mapped cache simulation
%rdx i | filter(,%rdx,4) &filter[i] | (%rdi,%rdx,4) &in[i]
0 | 0x00: 000 00 000 | 0x10: 000 10 000
1 | 0x04: 000 00 100 | 0x14: 000 10 100
2 | 0x08: 000 01 000 | 0x18: 000 11 000
3 | 0x0C: 000 01 100 | 0x1C: 000 11 100
0
?
?
v
Tag
Block
0
?
?
1
000
0x10, 0x14
0
?
?
Set 0
Set 1
Set 2
Set 3
miss
M= 8 bit addresses, B=8 bytes/block,
S=4 sets, E=1 Blocks/set
xxx
t=3
s=2
b=3
xx
xxx

## Slide 18: Direct-mapped cache simulation
%rdx i | filter(,%rdx,4) &filter[i] | (%rdi,%rdx,4) &in[i]
0 | 0x00: 000 00 000 | 0x10: 000 10 000
1 | 0x04: 000 00 100 | 0x14: 000 10 100
2 | 0x08: 000 01 000 | 0x18: 000 11 000
3 | 0x0C: 000 01 100 | 0x1C: 000 11 100
1
000
0x00, 0x04
v
Tag
Block
0
?
?
1
000
0x10 , 0x14
0
?
?
Set 0
Set 1
Set 2
Set 3
miss
M= 8 bit addresses, B=8 bytes/block,
S=4 sets, E=1 Blocks/set
xxx
t=3
s=2
b=3
xx
xxx

## Slide 19: Direct-mapped cache simulation
%rdx i | filter(,%rdx,4) &filter[i] | (%rdi,%rdx,4) &in[i]
0 | 0x00: 000 00 000 | 0x10: 000 10 000
1 | 0x04: 000 00 100 | 0x14: 000 10 100
2 | 0x08: 000 01 000 | 0x18: 000 11 000
3 | 0x0C: 000 01 100 | 0x1C: 000 11 100
M= 8 bit addresses, B=8 bytes/block,
S=4 sets, E=1 Blocks/set
xxx
t=3
s=2
b=3
xx
xxx
1
000
0x00, 0x04
v
Tag
Block
0
?
?
1
000
0x10 , 0x14
0
?
?
Set 0
Set 1
Set 2
Set 3
hit

## Slide 20: Direct-mapped cache simulation
1
000
0x00, 0x04
v
Tag
Block
0
?
?
1
000
0x10 , 0x14
0
?
?
Set 0
Set 1
Set 2
Set 3
%rdx i | filter(,%rdx,4) &filter[i] | (%rdi,%rdx,4) &in[i]
0 | 0x00: 000 00 000 | 0x10: 000 10 000
1 | 0x04: 000 00 100 | 0x14: 000 10 100
2 | 0x08: 000 01 000 | 0x18: 000 11 000
3 | 0x0C: 000 01 100 | 0x1C: 000 11 100
M= 8 bit addresses, B=8 bytes/block,
S=4 sets, E=1 Blocks/set
xxx
t=3
s=2
b=3
xx
xxx
hit

## Slide 21: Direct-mapped cache simulation
miss
%rdx i | filter(,%rdx,4) &filter[i] | (%rdi,%rdx,4) &in[i]
0 | 0x00: 000 00 000 | 0x10: 000 10 000
1 | 0x04: 000 00 100 | 0x14: 000 10 100
2 | 0x08: 000 01 000 | 0x18: 000 11 000
3 | 0x0C: 000 01 100 | 0x1C: 000 11 100
M= 8 bit addresses, B=8 bytes/block,
S=4 sets, E=1 Blocks/set
xxx
t=3
s=2
b=3
xx
xxx
1
000
0x00, 0x04
v
Tag
Block
0
?
?
1
000
0x10 , 0x14
0
?
?
Set 0
Set 1
Set 2
Set 3

## Slide 22: Direct-mapped cache simulation
1
000
0x00, 0x04
v
Tag
Block
0
?
?
1
000
0x10 , 0x14
1
000
0x18, 0x1C
Set 0
Set 1
Set 2
Set 3
miss
%rdx i | filter(,%rdx,4) &filter[i] | (%rdi,%rdx,4) &in[i]
0 | 0x00: 000 00 000 | 0x10: 000 10 000
1 | 0x04: 000 00 100 | 0x14: 000 10 100
2 | 0x08: 000 01 000 | 0x18: 000 11 000
3 | 0x0C: 000 01 100 | 0x1C: 000 11 100
M= 8 bit addresses, B=8 bytes/block,
S=4 sets, E=1 Blocks/set
xxx
t=3
s=2
b=3
xx
xxx

## Slide 23: Direct-mapped cache simulation
%rdx i | filter(,%rdx,4) &filter[i] | (%rdi,%rdx,4) &in[i]
0 | 0x00: 000 00 000 | 0x10: 000 10 000
1 | 0x04: 000 00 100 | 0x14: 000 10 100
2 | 0x08: 000 01 000 | 0x18: 000 11 000
3 | 0x0C: 000 01 100 | 0x1C: 000 11 100
M= 8 bit addresses, B=8 bytes/block,
S=4 sets, E=1 Blocks/set
xxx
t=3
s=2
b=3
xx
xxx
1
000
0x00, 0x04
v
Tag
Block
0
?
?
1
000
0x10 , 0x14
1
000
0x18, 0x1C
Set 0
Set 1
Set 2
Set 3
miss

## Slide 24: Direct-mapped cache simulation
%rdx i | filter(,%rdx,4) &filter[i] | (%rdi,%rdx,4) &in[i]
0 | 0x00: 000 00 000 | 0x10: 000 10 000
1 | 0x04: 000 00 100 | 0x14: 000 10 100
2 | 0x08: 000 01 000 | 0x18: 000 11 000
3 | 0x0C: 000 01 100 | 0x1C: 000 11 100
M= 8 bit addresses, B=8 bytes/block,
S=4 sets, E=1 Blocks/set
xxx
t=3
s=2
b=3
xx
xxx
miss
1
000
0x00, 0x04
v
Tag
Block
1
000
0x08, 0x0C
1
000
0x10 , 0x14
1
000
0x18, 0x1C
Set 0
Set 1
Set 2
Set 3

## Slide 25: Direct-mapped cache simulation
1
000
0x00, 0x04
v
Tag
Block
1
000
0x08, 0x0C
1
000
0x10 , 0x14
1
000
0x18, 0x1C
Set 0
Set 1
Set 2
Set 3
hit
%rdx i | filter(,%rdx,4) &filter[i] | (%rdi,%rdx,4) &in[i]
0 | 0x00: 000 00 000 | 0x10: 000 10 000
1 | 0x04: 000 00 100 | 0x14: 000 10 100
2 | 0x08: 000 01 000 | 0x18: 000 11 000
3 | 0x0C: 000 01 100 | 0x1C: 000 11 100
M= 8 bit addresses, B=8 bytes/block,
S=4 sets, E=1 Blocks/set
xxx
t=3
s=2
b=3
xx
xxx

## Slide 26: Direct-mapped cache simulation
1
000
0x00, 0x04
v
Tag
Block
1
000
0x08, 0x0C
1
000
0x10 , 0x14
1
000
0x18, 0x1C
Set 0
Set 1
Set 2
Set 3
%rdx i | filter(,%rdx,4) &filter[i] | (%rdi,%rdx,4) &in[i]
0 | 0x00: 000 00 000 | 0x10: 000 10 000
1 | 0x04: 000 00 100 | 0x14: 000 10 100
2 | 0x08: 000 01 000 | 0x18: 000 11 000
3 | 0x0C: 000 01 100 | 0x1C: 000 11 100
M= 8 bit addresses, B=8 bytes/block,
S=4 sets, E=1 Blocks/set
xxx
t=3
s=2
b=3
xx
xxx
hit
8 accesses
4 misses (cold), 4 hits
50% hit rate

## Slide 27: Direct-mapped cache simulation
1
000
0x00, 0x04
v
Tag
Block
1
000
0x08, 0x0C
1
000
0x10 , 0x14
1
000
0x18, 0x1C
Set 0
Set 1
Set 2
Set 3
%rdx i | filter(,%rdx,4) &filter[i] | (%rdi,%rdx,4) &in[i]
0 | 0x00: 000 00 000 | 0x10: 000 10 000
1 | 0x04: 000 00 100 | 0x14: 000 10 100
2 | 0x08: 000 01 000 | 0x18: 000 11 000
3 | 0x0C: 000 01 100 | 0x1C: 000 11 100
M= 8 bit addresses, B=8 bytes/block,
S=4 sets, E=1 Blocks/set
xxx
t=3
s=2
b=3
xx
xxx
hit
8 mem accesses
4 misses (cold), 4 hits
50% hit rate
hit
miss
miss
hit
hit
miss
miss

## Slide 28: Software View of Architecture State
Data
Instructions
CPU
Programmer-Visible State
  Does NOT change when we add caches
Contrast with microarchitecture state
  Microarchitecture is the specific implementation of an ISA
    HW designer decides what the microarchitecture looks like
  Caches: part of the microarchitecture state
PC
Registers
Memory
Object Code
Program Data
OS Data
Addresses
Stack
Condition
Codes
ALU

## Slide 29: Architecture vs. Microarchitecture
Physics
Devices
Circuits
Gates
Register-Transfer Level
Microarchitecture
Instruction Set Architecture (ISA)
Operating System/Virtual Machines
Programming Language
Algorithm
Application
Register-Transfer Level
%rip
L1 cache
memory address bits
Is the following part of Architecture or Microarchitecture?
cache valid bits
Notes: Interface between SW and HW

## Slide 30: Exam I Topics
Representation of Numbers
Integer Arithmetic
Basic x86-64 Architecture
Control Flow
Functions, Buffer Overflow
Arrays, Structs, Unions
Memory Hierarchy and Caching
Architecture vs. microarchitecture